## Slide 1
MAJOR PROJECT PRESENTATION
ANKIT KUMAR(14104071)
VIBHU KUMAR(14104074)
ABHISHEK KUMAR(14104093)
Supervisor
Dr. BALWINDER RAJ
Co-Supervisor
Dr. AMANDEEP SINGH
Design of Ternary SRAM using CNTFET

## Slide 2
INTRODUCTION
A carbon nanotube field-effect transistor (CNTFET) refers to a field-effect transistor that utilizes a single carbon nanotube or an array of carbon nanotubes as the channel material instead of bulk silicon in the traditional MOSFET structure.
The fabrication process can yield either a metallic or semiconducting tube depending on the angle of the arrangement of carbon atoms along the tube.
The angle of arrangement of carbon atoms is referred to as the chirality vector (n1, n2).
The chirality vector determines the diameter, the threshold voltage (VTH).

## Slide 3: Ternary logic
Ternary logic, a three-valued logic is any of several many-valued logic systems in which there are three truth values indicating true, false and some indeterminate third value.
A n-variable ternary valued function f (x1, . . . , xn) is a mapping f : S^n -> S, with the variable xi taking values from the set S ={0, 1, 2}.
However, the added complexity during fabrication and the overall unfamiliarity with multi-valued algebra has kept ternary computation a relatively smaller field.

## Slide 4: Ternary logic
y0=Negative Ternary Inverter
y1=Standard Ternary Inverter
y2=Positive Ternary Inverter

## Slide 5: Objectives
Studying about the basics of Carbon Nanotubes and Carbon Nanotubes FET
Setting up of environment.
Getting familiar with the HSPICE .
HSPICE simulation of various design models of Standard Ternary Inverter using CNTFET and their comparison.
Phase-1
Phase-2
HSPICE simulation of ternary circuits using MOSFET.
HSPICE simulation of SRAM using various cross-coupled Standard Ternary Inverter using CNTFET.
Comparison Of the SRAM made using CNTFET varying the various parameters.

## Slide 6: Methodology

## Slide 7: Work done till Phase 1
Studying about the basics of Carbon Nanotubes and Carbon Nanotubes FET
Reading of research papers-
A Novel CNTFET-Based Ternary Logic Gate Design by Sheng Lin, Yong-Bin Kim and Fabrizio Lombardi
Design of a ternary static memory cell using carbon nanotube-based transistors by K. You, K. Nepal
HSPICE Simulation of Standard Ternary Inverter using six CNTFET.
HSPICE Simulation of Standard Ternary Inverter using two CNTFET and two resistor.

## Slide 8: Standard Ternary Inverter using two CNTFET

## Slide 9: HSPICE simulation of Standard Ternary Inverter using two CNTFET
Chart: V(IN) VOLTS
Simulated Result
Paper Result

## Slide 10: Standard Ternary Inverter using six CNTFET

## Slide 11: HSPICE simulation of Standard Ternary Inverter using six CNTFET
Chart: V(IN) VOLTS
 | 0.89989 | 0.89983 | 0.89976 | 0.90157 | 0.89765 | 0.89946 | 0.88971 | 0.85486 | 0.80464 | 0.74862 | 0.70034 | 0.64818 | 0.59796 | 0.54774 | 0.49942 | 0.4587 | 0.45484 | 0.44697 | 0.39653 | 0.34627 | 0.19755 | 0.099037 | 0.010111 | 0.00030418 | 0.00011727 | 0.00099865 | 0.00088687

## Slide 12
Chart: V(IN) Volts
Comparison between the two design models of Standard Ternary Inverter
STI using 2 CNTFET
STI using 6 CNTFET

## Slide 13: Phase 2 work done so far
Study about the writing and reading process of SRAM.
Implementation of the SRAM using Standard ternary inverter(6 CNTFET design model) .
Implementation of SRAM using Negative ternary inverter and Positive ternary inverter.
Implementation of SRAM using 3 transistor inverter.
By varying parameter (Gate Length) we compare the performance of various SRAM.
By varying parameter (temperature) we compare the performance of various SRAM.

## Slide 14
Positive Ternary Inverter
Chart: 
Vout(Volts)
Vin(Volts)
Positive Ternary Inverter
Logic 0 logic 1 logic 2
Chirality vector-T2 (10,0) ,T1 (19,0)

## Slide 15
Negative Ternary Inverter
Chart: 
Vout(Volts)
Vin(Volts)
Negative Ternary Inverter
Logic 0 logic 1 logic 2
Chirality vector-T2 (19,0) ,T1 (10,0)

## Slide 16
Ternary Inverter using 3 transistors
Vout(Volts)
Vin(Volts)
Ternary Inverter using 3 transistors
Logic 0 logic 1 logic 2
Chart: 
Lg of P1=32nm (9,0)
Lg of N1=32nm (9,0)
Lg of N2=64nm (11,0)
No of tubes
P1=8 tubes
N1=20 tubes
N2= 2 tubes

## Slide 17
Threshold value for different chirality vector
Threshold Voltage
of P CNTFET(V)
Chirality vector
Chart: 
| 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22
Measured | -0.58 | -0.52 | -0.43 | -0.4 | -0.34 | -0.326 | -0.293 | -0.274 | -0.25
Calculated | -0.556 | -0.506 | -0.428 | -0.397 | -0.34 | -0.326 | -0.291 | -0.274 | -0.25
[1]

## Slide 18
SRAM using 6 CNTFET Standard Ternary Inverter
CNTFET-based ternary memory cell using STI [1]
CNTFET-based STI design [1]

## Slide 19
SRAM using 6 CNTFET STI write at Lg=20nm
Chart: 
Chart: 
Chart: 
Chart: 

## Slide 20
SRAM using 6 CNTFET STI read at Lg=20nm
Chart: 
Chart: 
Chart: 

## Slide 21
SRAM using 6 CNTFET STI write at Lg=32nm
Chart: 
Chart: 
Chart: 
Chart: 

## Slide 22
SRAM using 6 CNTFET STI read at Lg=32nm
Chart: 
Chart: 
Chart: 

## Slide 23
SRAM using 6 CNTFET STI write at Lg=45nm
Chart: 
Chart: 
Chart: 
Chart: 

## Slide 24
SRAM using 6 CNTFET STI read at Lg=45nm
Chart: 
Chart: 
Chart: 

## Slide 25
SRAM using Negative Ternary Inverter and Positive Ternary Inverter
CNTFET-based ternary memory cell using NTI and PTI [3]
CNTFET-based ternary inverter using NTI and PTI [3]
Chirality vector (10,0) (19,0) (13,0)

## Slide 26
SRAM using NTI and PTI write at Lg=20nm
Chart: 
Chart: 
Chart: 
Chart: 

## Slide 27
SRAM using NTI and PTI read at Lg=20nm
Chart: 
Chart: 
Chart: 

## Slide 28
SRAM using NTI and PTI write at Lg=32nm
Chart: 
Chart: 
Chart: 
Chart: 

## Slide 29
SRAM using NTI and PTI read at Lg=32nm
Chart: 
Chart: 
Chart: 

## Slide 30
SRAM using NTI and PTI write at Lg=45nm
Chart: 
Chart: 
Chart: 
Chart: 

## Slide 31
SRAM using NTI and PTI read at Lg=45nm
Chart: 
Chart: 
Chart: 

## Slide 32
SRAM using 3 Transistor Inverter
CNTFET-based ternary memory cell using 3 transistor inverter [2]
CNTFET-based ternar inverter using 3 transistors [2]
Lg of P1=32nm (9,0)
Lg of N1=32nm (9,0)
Lg of N2=64nm (11,0)
No of tubes
P1=8 tubes
N1=20 tubes
N2= 2 tubes

## Slide 33
SRAM using 3 Transistor Inverter write
Chart: 
Chart: 
Chart: 
Chart: 

## Slide 34
SRAM using 3 Transistor Inverter read
Chart: 
Chart: 
Chart: 

## Slide 35
Comparing SNM of SRAM using 6 CNTFET STI by varying the Gate length
Chart: 
Chart: 20nm 32nm 32nm(Paper) [1] 45nm Gate Length
| SNM(mV)
 | 123.89
 | 149.62
 | 154.2
 | 160.87
Size(nm) | SNM(mV)
20 | 123.89
32 | 149.62
32(Paper)[1] | 154.2
45 | 160.87

## Slide 36
Comparing SNM of SRAM using NTI and PTI by varying the Gate length
Chart: 20nm 32nm 45nm Gate Length
| SNM(mV)
 | 134.27
 | 157.82
 | 180.38
Size(nm) | SNM(mV)
20 | 134.27
32 | 157.82
45 | 180.38

## Slide 37
Comparing SNM of different designs at Lg=32nm
SRAM using SRAM using SRAM using
6 T STI NTI and PTI 3 T Inverter
Chart: SNM (mV)
| SNM
 | 149.62
 | 157.82
 | 84.87
Design | SNM(mV)
SRAM using 6T STI | 149.62
SRAM using NTI and PTI | 157.82
SRAM using 3T | 84.87

## Slide 38
Comparing average standby power of different designs at Lg=32nm
Design | Average standby power(Watt)
SRAM using 6T STI | 1.82E-07
SRAM using NTI and PTI | 1.03E-07
SRAM using 3 T | 4.85E-08

## Slide 39
Conclusion of different designs
Chart: 
SRAM using NTI and PTI has the highest SNM amongst the three designs but has higher average standby power than SRAM using 3T so there exists a tradeoff between SNM and average standby power when using different designs of ternary SRAM.
Design | SNM(mV)
SRAM using 6T STI | 149.62
SRAM using NTI and PTI | 157.82
SRAM using 3T | 84.87
Design | Average standby power(Watt)
SRAM using 6T STI | 1.82E-07
SRAM using NTI and PTI | 1.03E-07
SRAM using 3 T | 4.85E-08

## Slide 40
Comparing SNM of SRAM at different Temperature
Type(size) | SNM in mV at 25C | SNM in mV at 100C
SRAM(20nm) | 123.89 | 104.80
SRAM(32nm) | 150 | 125
SRAM(45nm) | 160.87 | 132.59
SRAM using 3T | 85 | 49
Chart: SNM(mV)
| SRAM(20nm) | SRAM(32nm) | SRAM(45nm) | SRAM using 3T
At 25C | 123.89 | 150 | 160.87 | 85
At 100C | 104.8 | 125 | 132.59 | 49

## Slide 41
Standby power of SRAM using 6 CNTFET STI by varying the Gate length at 25C
size | power in watt at 25C
20nm(0) | 3.60E-08
20nm(1) | 3.74E-07
20nm(2) | 7.76E-08
32nm(0) | 1.90E-09
32nm(1) | 1.90E-09
32nm(2) | 5.43E-07
45nm(0) | 1.02E-09
45nm(1) | 5.81E-07
45nm(2) | 1.21E-08
Chart: 
| 20nm(0) | 20nm(1) | 20nm(2) | 32nm(0) | 32nm(1) | 32nm(2) | 45nm(0) | 45nm(1) | 45nm(2)
power in watt at 25C | 3.6e-08 | 3.74e-07 | 7.76e-08 | 1.9e-09 | 1.9e-09 | 5.43e-07 | 1.017e-09 | 5.81e-07 | 1.206e-08

## Slide 42
Standby power of SRAM using 6 CNTFET STI by varying the Gate length at 100C
Chart: Power(Watt)
| 20nm(0) | 20nm(1) | 20nm(2) | 32nm(0) | 32nm(1) | 32nm(2) | 45nm(0) | 45nm(1) | 45nm(2)
power at 100C | 1.81e-09 | 6.57e-07 | 1.143e-08 | 3.02e-09 | 2.78e-09 | 3.02e-07 | 3.06e-09 | 8.58e-07 | 1.08e-08
Size | Power in watt at 100C
20nm(0) | 1.81E-09
20nm(1) | 6.57E-07
20nm(2) | 1.14E-08
32nm(0) | 3.02E-09
32nm(1) | 2.78E-09
32nm(2) | 3.02E-07
45nm(0) | 3.06E-09
45nm(1) | 8.58E-07
45nm(2) | 1.08E-08

## Slide 43
Standby power of SRAM using NTI and PTI by varying the Gate length at 25C
Size | Power in at 25C
20nm(0) | 4.68E-09
20nm(1) | 2.45E-07
20nm(2) | 7.46E-09
32nm(0) | 3.02E-09
32nm(1) | 2.78E-09
32nm(2) | 3.02E-07
45nm(0) | 6.28E-08
45nm(1) | 7.40E-07
45nm(2) | 1.07E-07
Chart: Power(Watt)
| 20nm(0) | 20nm(1) | 20nm(2) | 32nm(0) | 32nm(1) | 32nm(2) | 45nm(0) | 45nm(1) | 45nm(2)
power at 25C | 4.68e-09 | 2.45e-07 | 7.46e-09 | 3.02e-09 | 2.78e-09 | 3.02e-07 | 6.28e-08 | 7.4e-07 | 1.07e-07

## Slide 44
Standby power of SRAM using NTI and PTI by varying the Gate length at 100C
Chart: Power(watt)
| 20nm(0) | 20nm(1) | 20nm(2) | 32nm(0) | 32nm(1) | 32nm(2) | 45nm(0) | 45nm(1) | 45nm(2)
power at 100C | 1.35e-09 | 1.242e-06 | 1.73e-08 | 1.33e-08 | 9.7e-07 | 4.9e-09 | 2.88e-09 | 5.58e-07 | 1.035e-08
Size | power in watt at 100C
20nm(0) | 1.35E-09
20nm(1) | 1.24E-06
20nm(2) | 1.73E-08
32nm(0) | 1.33E-08
32nm(1) | 9.70E-07
32nm(2) | 4.90E-09
45nm(0) | 2.88E-09
45nm(1) | 5.58E-07
45nm(2) | 1.04E-08

## Slide 45
Standby power of SRAM using 3 transistor Inverter at 25C
Logic | Power in watt at 25C
0 | 6.93E-08
1 | 7.40E-08
2 | 2.20E-09
Chart: Logic 0 Logic 1 Logic 2
| Power at 25C
 | 6.93e-08
 | 7.4e-08
 | 2.2e-09

## Slide 46
Standby power of SRAM using 3 transistor Inverter at 100C
Chart: Logic 0 Logic 1 Logic 2
| power at 100C
 | 1.89e-07
 | 1.88e-07
 | 1.89e-09
Logic | Power in watt at 100C
0 | 1.89E-07
1 | 1.88E-07
2 | 1.89E-09

## Slide 47
Conclusion of SRAM using 6 CNTFET STI
Chart: 
SIZE(nm) | SNM(mV)
20 | 123.89
32 | 149.62
32(Paper)[1] | 154.2
45 | 160.87
SIZE (nm) | Standby power in watt
20 | 1.63E-07
32 | 1.82E-07
45 | 1.98E-07
As we scale down technology SNM reduces which is a disadvantage but the standby power consumption also reduces so there exists tradeoff between SNM and power as we scale down technology

## Slide 48
Conclusion of SRAM using NTI and PTI
Chart: 
As we scale down technology SNM reduces which is a disadvantage but the standby power consumption also reduces so there exists tradeoff between SNM and power as we scale down technology
Size(nm) | SNM(mV)
20 | 134.27
32 | 157.82
45 | 180.38
SIZE (nm) | Power in watt
20 | 8.57E-08
32 | 1.03E-07
45 | 3.03E-07

## Slide 49: References
Design of a Ternary Memory Cell Using CNTFETs Sheng Lin, Student Member, IEEE, Yong-Bin Kim, Senior Member, IEEE, and Fabrizio Lombardi, Fellow, IEEE
Design of a ternary static memory cell using carbon nanotube-based transistors K. You, K. Nepal Department of Electrical Engineering, Bucknell University, Lewisburg, PA 17837, USA
2015 Interational Conference on Communication,Control and Intelligent Systems (CCIS) Design, Analysis and Comparison between CNTFET Based Terary SRAM Cell and PCRAM Cell
A Novel CNTFET-Based Ternary Logic Gate Design Sheng Lin, Yong-Bin Kim and Fabrizio Lombardi Department of Electrical and Computer Engineering Northeastern University Boston, MA, USA